## Slide 1: DIGITAL ELECTRONICS: ECE 213
Prepared By: Irfan Ahmad Pindoo
Assistant Professor
VLSI Design, ECE
School of Computer Science and Engineering
Topic: Sequential Circuits, Latches and Flip flops
UNIT IV: Introduction to Sequential Circuits
Lecture No.: 26

## Slide 2: Introduction to Sequential Circuits
Sequential circuits are those in which the output depends not only on the present inputs, but also on the previous output state and/or the previous inputs.

## Slide 4: Difference between Combinational and Sequential Circuits
Combinational Circuits | Sequential Circuits
The output depends only upon the present inputs | output depends not only on the present inputs, but also on the previous output state and/or the previous inputs
No feedback | Feedback available from output to input
No ability to store | Ability to store
Easier to design, use and handle | not easier to design, use and handle
No clock signal | Clock signals are required for triggering purposes
Faster | slower than combinational circuits
Elementary building block: Logic gates | Elementary building block: Flip flops
Examples: Adder, Subtractor, Magnitude comparator, Multiplexer, Decoder, etc. | Examples: Latches, flip flops, counters, registers,etc.

## Slide 5: QUICK QUIZ (POLL)
Which of the following is NOT the combinational circuit?
magnitude comparator
multiplexer
parity generator circuit
Flip flop

## Slide 6: Basic Storage Element: Latch
A storage element in a digital circuit can maintain a binary state indefinitely (as long as power is delivered to the circuit), until directed by an input signal to switch states.
Storage elements that operate with signal levels (rather than signal transitions) are referred to as latches; those controlled by a clock transition are flip-flops.
Because they are the building blocks of flip-flops, so, we will consider the fundamental storage mechanism used in latches before considering flip-flops.

## Slide 7: SR Latch
The SR latch is a circuit with two cross-coupled NOR gates or two cross-coupled NAND gates, and two inputs labeled S for set and R for reset.
The latch has two useful states:
  When output Q = 1 and = 0, the latch is said to be in the set state.
  When Q = 0 and = 1, it is in the reset state.
Outputs Q and are normally the complement of each other. Otherwise, the device will enter an unpredictable or undefined state or a metastable state.

## Slide 8: QUICK QUIZ (POLL)
What is the output state in SR latch at Q = 1 and = 0
set
reset
memory
indeterminate

## Slide 9: SR NOR Latch

## Slide 10: SR NOR Latch

## Slide 11: QUICK QUIZ (POLL)
Which of the following state is invalid/indeterminate in SR NOR latch?
S=1, R= 0
S=0, R= 1
S=0, R= 0
S=1, R= 1

## Slide 12: SR NAND Latch

## Slide 14: SR NAND Latch
Because the NAND latch requires a 0 signal to change its state, it is sometimes referred to as an latch.
The primes (or, sometimes, bars over the letters) designate the fact that the inputs must be in their complement form to activate the circuit.

## Slide 15: QUICK QUIZ (POLL)
Which of the following state is invalid/indeterminate in SR NAND latch?
S=1, R= 0
S=0, R= 1
S=0, R= 0
S=1, R= 1

## Slide 16: SR Latch with control input
The operation of the basic SR latch can be modified by providing an additional input signal that determines (controls) when the state of the latch can be changed by determining whether S and R can affect the circuit.

## Slide 17: SR Latch with control input
The operation of the basic SR latch can be modified by providing an additional input signal that determines (controls) when the state of the latch can be changed by determining whether S and R can affect the circuit.

## Slide 18: QUICK QUIZ (POLL)
What is the output state in SR enabled NAND based latch at S=1, R= 0, and En=0?
Q= set
Q=reset
Q=memory
Q=indeterminate

## Slide 19: D Latch (Transparent Latch)
One way to eliminate the undesirable condition of the indeterminate state in the SR latch is to ensure that inputs S and R are never equal to 1 or 0 at the same time. This is done in the D latch.

## Slide 20: D Latch (Transparent Latch)
One way to eliminate the undesirable condition of the indeterminate state in the SR latch is to ensure that inputs S and R are never equal to 1 or 0 at the same time. This is done in the D latch.

## Slide 21: D Latch (Transparent Latch)
The D latch receives that name from its ability to hold data in its internal storage. It is suited for use as a temporary storage.
The binary information present at the data input of the D latch is transferred to the Q output when the enable input is asserted.
The output follows changes in the data input as long as the enable input is asserted. This situation provides a path from input D to the output, and for this reason, the circuit is often called a transparent latch.
When the enable input signal is de-asserted, the binary information that was present at the data input at the time the transition occurred is retained (i.e., stored) at the Q output until the enable input is asserted again.

## Slide 22: QUICK QUIZ (POLL)
In D flip-flop, D stands for _____________
a) Distant
b) Data
c) Desired
d) Delay