## Slide 1: Unit-5 Combinational Circuit Adders Subtractor Decoder-Encoder Multiplexers-Demultiplexers Comparator Parity IC Family

## Slide 3: Combinational Circuits
output depends only on the present input
The combinational circuit do not use any memory.
The previous state of input does not have any effect on the present state of the circuit.

## Slide 4: Half Adder
A combinational logic circuit with two inputs and two outputs.
The half adder circuit add two single bit Cary number
This circuit has two outputs carry and sum.
S(A, B) = ∑m (1, 2)
CY(A, B) = ∑m (3)

## Slide 5: Full Adder (1-bit Adder)
A combinational logic circuit with 3 inputs and 2 outputs.
The Full adder circuit add 3 single bit Cary number
This circuit has two outputs carry and sum.
Sum(A, B,C) = ∑m (1, 2, 4, 7)
Cout(A, B, C) = ∑m (3,5,6,7)

## Slide 6
For Cout
Cout=AB+BC+AC

## Slide 7: Full Adder using Half Adder
FA
Sum= A⊕B⊕C
Carry=AB+(A⊕B)C
HA
Sum= A⊕B
Carry=AB

## Slide 8: Half Subtractor
Combinational circuit perform binary Subtraction
Accepts 2 input and Two output Difference and Borrow
D(A, B) = ∑m (1, 2)
Br(A, B) = ∑m (1)

## Slide 9: Full Subtractor
Performs subtraction of 3 bits
This circuit has three inputs and two outputs.
The three inputs A, B and C, denote the minuend, subtrahend, and previous borrow, respectively.
The two outputs, D and Bout
Sum(A, B,C) = ∑m (1, 2, 4, 7)
Bout(A, B,C) = ∑m (1,2,3,7)

## Slide 10
Bout = A’B’C + A’BC’ + A’BC + ABC
= C(AB + A’B’) + A’B(C + C’)
= C( A XNOR B) + A’B
= C (A XOR B)’ + A’B

## Slide 11: Full Subtractor using Half Subtractor
FS
Sum= A⊕B⊕C
Carry=A’B+(A⊕B)’C
HS
Sum= A⊕B
Carry=A’B

## Slide 12
Design a 3 input digital circuit produces high output for two or more binary input high
A | B | C | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 13
Design a 3 input digital circuit produces high output for ODD decimal equivalent
A | B | C | Y
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 

## Slide 14: 1-BIT Magnitude Comparator
1-Bit Magnitude Comparator
A
B
GT
EQ
LT
GT
EQ
LT
GT=AB’
EQ=A’B’+AB
LT=A’B

## Slide 15: 2-BIT Magnitude Comparator

## Slide 16: Multiplexer
A combinational circuit has maximum of 2n data inputs, ‘n’ selection lines and single output line.
One of these data inputs will be connected to the output based on the values of selection lines
It is a data selector device
Size of multiplexer is :1
2:1 Multiplexer
I0
I1
Y
S
=S’I0 + SI1
0
1

## Slide 17: 4:1 Multiplexer
Selection Lines |  | Output
S1 | S0 | Y
0 | 0 | I0
0 | 1 | I1
1 | 0 | I2
1 | 1 | I3

## Slide 18: Expression implementation with Multiplexer
Y(A, B,C) = ∑m (1, 3, 5, 6) implement with 4:1 multiplexer
Any 2 input (AB/BC/AC) select line
Rearrange equation with selection line
I0 I1 I2 I3
0
1
A
A’
Y(A, B,C) = ∑m (1, 2, 4, 5) implement with 4:1 multiplexer
Any 2 input (AB/BC/AC) select line
Rearrange equation with selection line
I0 I1 I2 I3
C
C’
1
0

## Slide 19: Logic Gate implementation with 2:1 Multiplexer
AND GATE
NAND GATE
OR GATE
NOR GATE

## Slide 20: Logic Gate implementation with 2:1 Multiplexer
XOR GATE
XNOR GATE
NOT GATE

## Slide 21: Full Adder implementation with 4:1 Multiplexer
S(A, B, Cin) = ∑(1, 2, 4, 7) = m1 + m2 + m4 +m7 = A’B’Cin + A’BC’in + AB’C’in + ABCin = A.(B’C’in) + A’.(B’Cin) + A’.(BC’in) + A.(B’C’in) (1)
4:1 Mux equation Y = I0S’1S’0 + I1S’1S0 + I2S1S’0 + I3S1S0 (2)
Compare (1) and (2) with S1 = B, S0 = Cin
I0 = A, I1 = A’, I2 = A’, I3 = A.
Cout(A, B, Cin) = ∑(3, 5, 6, 7) = m3 + m5 + m6 + m7 = A’BCin + AB’Cin + ABC’in + ABCin = (A’ + A) BCin + AB’Cin + ABC’in + 0.AB’C’in = 0.(B’C’in) + A.(B’Cin) + A.(BC’in) + 1.(BCin) (3)
4:1 Mux equation Y = I0S’1S’0 + I1S’1S0 + I2S1S’0 + I3S1S0 (4)
Comparing equation (1) and (3) with S1 = B, S0 = Cin.
I0 = 0, I1 = A, I2 = A, I3 = 1

## Slide 22: 8:1 Multiplexer
S2 | S1 | S0 | Out
0 | 0 | 0 | I0
0 | 0 | 1 | I1
0 | 1 | 0 | I2
0 | 1 | 1 | I3
1 | 0 | 0 | I4
1 | 0 | 1 | I5
1 | 1 | 0 | I6
1 | 1 | 1 | I7
Out=S2’S1’S0’I0 + S2’S1’S0I1+ S2’S1S0’I2+ S2’S1S0I3
S2S1’S0’I4+ S2S1’S0I5+ S2S1S0’I6+ S2S1S0I7

## Slide 23: Full adder using 8:1 Mux
S(A, B, Cin) = ∑(1, 2, 4, 7)
Cout(A, B, Cin) = ∑(3, 5, 6, 7)
High input for present minterm, low input for minterm not present

## Slide 25: 4:1 Mux using 2:1 Mux
S1 (MSB) | S0(LSB) | Out
0 | 0 | I0
0 | 1 | I1
1 | 0 | 12
1 | 1 | I3
8:1 Mux using 4:1 and 2:1 Mux

## Slide 26: Demultiplexer
switch one common input line to one of several output line based on select input
It is data distributor
Size of demux 1: Example 1:4, 1:8, 1:16….. Demultiplexer
Selection Inputs |  | Outputs |  |  | 
S1 | S0 | Y3 | Y2 | Y1 | Y0
0 | 0 | 0 | 0 | 0 | I
0 | 1 | 0 | 0 | I | 0
1 | 0 | 0 | I | 0 | 0
1 | 1 | I | 0 | 0 | 0

## Slide 27: Decoder
A combinational circuit that has ‘n’ input lines and maximum of 2n output lines.
One of these outputs will be active High based on the combination of inputs present, when the decoder is enabled.
The outputs of the decoder are min terms of ‘n’ input variables lines when it is enabled
Size of Decoder are 2:4, 3:8, 4:16….
A1 | A0 | Y3 | Y2 | Y1 | Y0
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0

## Slide 28: Full Adder using 3:8 Decoder
S = A’B’C + A’BC’ + AB’C’ + ABC = Σ(1,2,4,7)
CY = A’BC +AB’C +ABC’+ABC= Σ (3, 5, 6, 7)
Full Subtractor using 3:8 Decoder
DIFFERENCE = A’B’C + A’BC’ + AB’C’ + ABC = Σ(1,2,4,7)
BORROW = A’B’C +A’BC’ +A’BC+ABC= Σ (1, 2, 3, 7)
Y

## Slide 31: 3:8 decoder using 2:4 decoder
Decoder with Enable
One of outputs will be ‘1’ when enable, E is ‘1’
A2 | A1 | A0 | HIGH OUTPUT
0 | 0 | 0 | Y0
0 | 0 | 1 | Y1
0 | 1 | 0 | Y2
0 | 1 | 1 | Y3
1 | 0 | 0 | Y4
1 | 0 | 1 | Y5
1 | 1 | 0 | Y6
1 | 1 | 1 | Y7

## Slide 32: 4:16 decoder
A3 | A2 | A1 | A0 | HIGH OUTPUT
0 | 0 | 0 | 0 | Y0
0 | 0 | 0 | 1 | Y1
0 | 0 | 1 | 0 | Y2
0 | 0 | 1 | 1 | Y3
0 | 1 | 0 | 0 | Y4
0 | 1 | 0 | 1 | Y5
0 | 1 | 1 | 0 | Y6
0 | 1 | 1 | 1 | Y7
1 | 0 | 0 | 0 | Y8
1 | 0 | 0 | 1 | Y9
1 | 0 | 1 | 0 | Y10
1 | 0 | 1 | 1 | Y11
1 | 1 | 0 | 0 | Y12
1 | 1 | 0 | 1 | Y13
1 | 1 | 1 | 0 | Y14
1 | 1 | 1 | 1 | Y15
4:16 Decoder
A3
A2
A1
A0
Y0
Y15
EN

## Slide 33: 4:16 decoder using 3:8 decoder
A3 | A2 | A1 | A0 | HIGH OUTPUT
0 | 0 | 0 | 0 | Y0
0 | 0 | 0 | 1 | Y1
0 | 0 | 1 | 0 | Y2
0 | 0 | 1 | 1 | Y3
0 | 1 | 0 | 0 | Y4
0 | 1 | 0 | 1 | Y5
0 | 1 | 1 | 0 | Y6
0 | 1 | 1 | 1 | Y7
1 | 0 | 0 | 0 | Y8
1 | 0 | 0 | 1 | Y9
1 | 0 | 1 | 0 | Y10
1 | 0 | 1 | 1 | Y11
1 | 1 | 0 | 0 | Y12
1 | 1 | 0 | 1 | Y13
1 | 1 | 1 | 0 | Y14
1 | 1 | 1 | 1 | Y15

## Slide 34: 4:16 decoder using 2:4 decoder
A3 | A2 | A1 | A0 | HIGH OUTPUT
0 | 0 | 0 | 0 | Y0
0 | 0 | 0 | 1 | Y1
0 | 0 | 1 | 0 | Y2
0 | 0 | 1 | 1 | Y3
0 | 1 | 0 | 0 | Y4
0 | 1 | 0 | 1 | Y5
0 | 1 | 1 | 0 | Y6
0 | 1 | 1 | 1 | Y7
1 | 0 | 0 | 0 | Y8
1 | 0 | 0 | 1 | Y9
1 | 0 | 1 | 0 | Y10
1 | 0 | 1 | 1 | Y11
1 | 1 | 0 | 0 | Y12
1 | 1 | 0 | 1 | Y13
1 | 1 | 1 | 0 | Y14
1 | 1 | 1 | 1 | Y15

## Slide 35: 4:2 Encoder

## Slide 36: Parity Generator Circuit
Even Parity Generator
If odd number of ones present in the input, then even parity bit, P should be ‘1’ so that the resultant word contains even number of ones.
Binary Input WXY | Even Parity bit P
000 | 0
001 | 1
010 | 1
011 | 0
100 | 1
101 | 0
110 | 0
111 | 1
Odd Parity Generator
If even number of ones present in the input, then odd parity bit, P should be ‘1’ so that the resultant word contains odd number of ones
Binary Input WXY | Odd Parity bit P
000 | 1
001 | 0
010 | 0
011 | 1
100 | 0
101 | 1
110 | 1
111 | 0

## Slide 37: Parity Checker Circuit
Even parity checker checks error in the transmitted data, which contains message bits along with even parity.

## Slide 38
IC Families
Logic family are digital integrated circuit devices which are constructed with a combination of electronic gates.
A family has its own power supply voltage and group potential; distinct logic levels.
Diode Logic (DL) logic is implemented with the use of resistors and diodes.
Resistor-Transistor Logic (RTL) logic is implemented with the use of transistors and resistors
Diode-Transistor Logic (DTL) logic is implemented with the use of diodes and transistors.
Transistor-Transistor Logic (TTL) logic are implemented with transistors
Emitter Coupled Logic (ECL) logic are implemented with transistors
Complementary Metal Oxide Semiconductor Logic (CMOS) logic are implemented with MOSFET

## Slide 39
Fan out: It specifies the number of standard loads that the output of the gate can drive without affecting its normal operation.
Fan in: This is the number of inputs of a logic gate.
Power Dissipation: This is the power supplied required to operate the gate.
Propagation delay Time delay between the occurrence of change in the logical level at the input and before it is reflected at the output
Noise margin: This is the maximum noise voltage added to the input signal of digital circuit that does not cause an undesirable change in the circuit output